For Immediate Release	CONTACT:

Caressa Prescott

Communications Manager

770-813-6185

c.prescott@agcocorp.com

# Hesston® Series Large Square Balers

# The Pioneer Keeps Setting the Standard

DULUTH, GA –January 2007 — New Hesston® Series large square balers from Massey Ferguson® take efficiency, capacity and serviceability to new levels. The Model 2190 builds solid 4 x 4 bales, and the Model 2170 builds 3 x 4 bales that are the result of a total review of the famed Hesston large square baler concept. These new models with their proven double knotter work harder, faster and easier without sacrificing durability and simplicity of operation. Hay goes in faster and smoother than ever before, and the operator has more control and command than ever before, not to mention spending less time on service than ever before. Even the new shielding with its smooth curves has purpose as dust and chaff slide off, and a single release on either side of the baler reveals all service points.

"We changed the look of these new balers, but it is the changes inside that make them truly superior to anything on the market," says Eric Raby, vice president, Livestock, Dairy, and Rural Lifestyle Marketing.  "Our engineers took our existing large square balers apart and put them back together with greater strength, greater ease of service and greater productivity. Capacity has increased significantly without sacrificing hay quality retention, thanks to the improved feeder design, a higher speed gearbox and other improvements."

Improved efficiencies through better design and engineering start with several innovations at the pickup. The new, lower profile, 4-bar pickup bar, previously found on 3 x 4 and 3 x 3 balers, is now also available on the Model 2190 4 x 4. It retains leaves better than the old 5-bar design. Both new balers feature heavier pickup tines and a new torsion bar flotation system that eliminates crop catching and trash collecting springs. Patent pending quad augers feed hay smoothly and quickly to packer fingers, eliminating bunching and over-ride that can occur with only a single set of stub augers. On the cutter version of the new balers, a single overhead auger combined with the base stub augers offer the same handling benefits to the rotor feeding system. Even the positioning of the tongue and pickup has been redesigned to handle extra crop volume.

While the smoother feed is important, it is the increased speed of the total system that makes capacity improvements of 30% for the new Model 2190 4 x 4 and 10% for the new Model 2170 3 x 4 balers. Gearbox speed has increased plunger speed from 25 strokes to 33 strokes per minute with the Model 2190 and from 42 to 47 strokes per minute on the Model 2170. The new balers retain the Hesston Series proven single gearbox with its chain drive design.

"We have looked at alternative drive systems for nearly three decades, since Hesston first introduced large square baling, but there simply isn't anything more efficient or easier to maintain than our chain drive system," says Jeff Noll, marketing specialist, Hay and Forage Equipment. "Some other brands of balers have multiple gear boxes and four different ways a sheared bolt can be replaced, three of which can result in disaster. With the Hesston Series, we have only two shear bolts in the entire baler, and simply lining up the holes and re-installing the bolt assures proper timing. It is fast."

Computer aided redesign and availability of new components, sometimes with higher quality steel or other modifications, produced a stronger, more durable baler. Flywheel weight on both balers has increased by 76 lbs. for greater plunger inertia, while the slipclutches have five discs instead of four for longer clutch life. Wherever possible, greaseable sleeves have been replaced with sealed bearings and roller ball bearings replaced with tapered roller bearings. The result is overall reduced lube points while extending the standard 10-hour lube period to 50 hours.

"The redesign means less time spent maintaining and more time spent baling," says Noll. "Even the centralized hand-pump lube system for the knotter has been enhanced with an auto-lube system that can be adjusted from the cab for more or less frequent lubrication as deemed necessary by the operator."

The new design also allows the operator to reveal all service points and twine storage with the release of a single panel on each side of the baler. Simply moving twine ball storage from vertical to a 30( positioning opened up otherwise difficult to reach service points. Like the large hood over the flywheel, all panels open easily on gas struts.

"The goal in the design of this new generation in big square balers was to make a more productive system, and we succeeded in simplicity, durability and capacity," says Raby. "With our ISOBUS ready design, the color AGCO Global Technologies Console I control monitor is even more operator friendly. It offers improved viewing in variable light conditions, easy access for baler function monitoring and in-cab function adjustment. These balers are not only bigger and faster, they are indeed smarter too."

Visit www.masseyferguson.com for full details on Hesston Series Large Square Balers from Massey Ferguson.

AGCO Corporation, headquartered in Duluth, Georgia, is a global manufacturer and distributor of agricultural equipment and related replacement parts.  AGCO products are distributed in more than 140 countries.  AGCO offers a full product line including tractors, combines, hay tools, sprayers, forage, tillage equipment and implements through more than 3,600 independent dealers and distributors around the world.  AGCO products are distributed under the various well-known brand names AGCO, Challenger, Fendt®, Gleaner, Hesston, Massey Ferguson, New Idea, RoGator, Spra-Coupe, Sunflower, Terra-Gator, Valtra, and White(tm) Planters.  AGCO provides retail financing through AGCO Finance.  In 2005, AGCO had net sales of $5.4 billion. Please visit our website at www.agcocorp.com.

# # # # #

ENCLOSED PHOTO: Hesston Series 2190 from Massey Ferguson Large Square Baler

PHOTO CAPTION: As part of the new Hesston Series from Massey Ferguson, the Model 2190 builds solid 4 X 4 bales, while the Model 2170 produces a slightly smaller 3 X 4 bale. Both models feature even higher capacity combined with your Massey Ferguson dealer’s commitment to customer satisfaction.

# # #

To download this and other Massey Ferguson news releases, please visit www.masseyferguson.com. (Scroll over “About MF” and then click on “Press Releases.")

# Text boxes

AGCO Corporation

4205 River Green Parkway Duluth, GA USA 30096-2563

www.agcocorp.com

P: 770-813-9200

Massey Ferguson( Product News Release

Massey Ferguson( Product News Release